Autologic diagnostics tool for MERCEDES BENZ

Update: Can not update.

Language :English

Warranty: One year warranty. Multiplexer Can Not Be Dismantled. Otherwise, It Will Be Not Under Warranty
Coverage: Autologic MERCEDES-BENZ covers vehicles from 1995 onwards

Specification:

SCN Coding (Software Calibration Number)

SCN coding is used by an increasing number of ECU's as the method for coding. SCN codingreplaces the old method of multiple options, where the user selects and edits each coding option. SCN coding codes the control module with predefined coding based on the VIN and part number.

Full Variant Coding

Autologic offers full variant coding on all modules. This gives users the ability to perform variant coding on any control module. Any new or existing control modules can be coded to suit the options or requirements of that specific car. Retrofitting of components is also possible.

Special Functions

The Autologic tool provides special functions which the dealer tool cannot. Examples of these include TV activation and air bag unlocking functions.

TVs by default are restricted from being viewed whilst the car is in motion. Using Autologic this limitation can be removed on a number of vehicles. Similarly, an airbag which is normally interlocked to a vehicle can be unlocked to allow coding to be changed or the airbag fitted to another vehicle.

Injector Coding / Classification

Injector coding I classification is an important function on the Mercedes software. This function will allow the user to replace the injectors for new and used parts but more importantly the ECU will know the exact specification of the injector fitted. This process is critical as the IMA code is used by the controller to determine the injector fitted, which will in turn determine how the fuel is delivered.

WSP Key Coding

The WSP (Immobiliser) module has a unique method of coding the keys. This method requires the new key to be put in the ignition then a random generated number is displayed on Autologic and the correct code is then entered using Autologic. All vehicles fitted with a WSP will require this method to code new keys.

Working photo shown:

Packing List:

1pc x Autologic vehicle diagnostics tool for MERCEDES-BENZ

Any questions, please don't hesitate to contact us.

Email:sales02@cardiag.co.uk

Skype:cardiag.co.uk

Yahoo:cardiag.service@yahoo.com